## Slide 1: AIM National Aquatic Monitoring Framework: Lentic Monitoring Methods
Tess Webb and Justin Jimenez
In collaboration with:
Joanna Lemly, Ruth Whittington, Katrina Castro CNHP
Melissa Dickard, Cassie Mellon, BLM
Notes: Justin introduces

## Slide 2: Overview
AIM Strategy
Lentic Riparian-Wetland Areas
Lentic AIM protocol methods
Pilot Season

## Slide 3: What is AIM?
The goal of the Assessment, Inventory, and Monitoring Strategy (AIM) is to reach across programs, jurisdictions, stakeholders, and agencies to provide standardized information to inform management decisions (Toevs et al 2011)
Notes: Overall AIM Strategy: Standardized approach to monitoring
Promote integrated, cross-program resource inventory, assessment and monitoring at multiple scales of management
Collect consistent, comparable and quantitative monitoring data to understand renewable resource condition and trend

## Slide 4: Key Principles of the AIM Strategy
5 key elements for collecting standardized & defensible data
Quantitative core indicators and methods
  What to measure and how to measure
Statistically valid sample designs
  Where and how to locate sample sites
Integration of remote sensing technologies
  How to obtain spatially explicit resource information
Data management plans
  Improve data quality, availability, and usability
Structured implementation
  Question driven approach
Notes: AIM program primarily focuses on collecting CONSISTENT, COMPARABLE (standardized) data across vast LANDSCAPES
Collect consistent, comparable and quantitative monitoring data to understand renewable resource condition and trend
Overall AIM Strategy:
Promote integrated, cross-program resource inventory, assessment and monitoring at multiple scales of management
Collect consistent, comparable and quantitative monitoring data to understand renewable resource condition and trend

## Slide 5: AIM Monitoring
Probability-based monitoring:
Measurements/estimation of condition and trends at randomly selected sites where every member of the target population has a known probability of being selected
Targeted monitoring:
Measurement/estimation of condition and trends at deliberately selected sites, often referred to as targeted sites
Notes: Currently lotic and terrestrial implement both forms of monitoring and lentic has the potential to incorporate both as well* Principles the same as lotic and lentic.

## Slide 6: Terrestrial & Lotic AIM
Notes: Terrestrial and Lotic AIM protocols are well established and being used. 20,000 Terrestrial and 2500 lotic sites have been visited across all BLM lands
Photo source:
https://aim.landscapetoolbox.org/data-collection/field-sampling/
http://www.usu.edu/buglab/Content/SWM_WRSA_2Feb2015_NoAnimation.pdf

## Slide 7: What about the systems where land and water meet?
Notes: No protocol observes complexities of these areas.
Lentic-wetland-riparian areas cover only 1% of BLM land, but their ecosystem services are so important.

## Slide 8: DRAFT Lentic Monitoring Methods
Developed through an interdisciplinary collaboration between:
BLM National Operations Center
Colorado Natural Heritage Program at Colorado State University
U.S. Forest Service.
Notes: An interagency effort with BLM, USFS, CNHP to create a draft protocol. It was completed in April of 2018.
Many of the methods were adapted from other existing BLM protocols.

## Slide 9: Lentic Systems Including wet meadows, riparian floodplains, springs, sloughs, fens
Systems with evidence of key lentic characteristics.
Support perennial vegetation.
Areas with water shallower than 50cm.
Minimum size: 300 m2
Notes: This procol is meant for a variety of different systems, wetland, riparian, lentic systems. Which includes wet meadows, floodplains springs etc.. Evidence of hydric soils, hydrophtic vegetation, and some degree of regular inundation or saturation.
This protocol isn’t intended for aquatic environments its intended for transitional zones. *Water depth only excludes portions of lentic areas with deep water, not the entire lentic area. For example, a lake can’t be sampled, but the lentic fringes can.
The minimum size is 300m2. This means we have a large variety of systems that we can monitor with this protocol- which we have to accomodate.

## Slide 10: Lentic Monitoring: Plot Layouts
25 m
25 m
25 m
25 m
a) Spoke Layout
b) Transverse Layout
c) Diagonal Layout
d) Linear Layout
Plot size:
300 – 3,000 m2
Plot can encompass an entire small wetland, or only a portion of a larger wetland.
Four different layouts to capture the range of wetland shapes.
Notes: It’s important to mention that we aren’t trying to monitor an entire wetland or lentic areas, but rather monitoring trends or condition of a specific location within a system.
Since the protocol encompasses a variety of systems there’s no one size fits all for laying out monitoring plots.
The preferred method is the Spoke Laypout which consists of three 25 m transects in a peace sign. But, we offer alternatives since not every system will fit a spoke. Transition- once the designated area has been defined there are a variety of indicators that can be collected.

## Slide 11: Key Characteristics
Hydrology
Vegetation
Soils
Notes: Soils and Hydrology are fundamental components of lentic systems, but are hard to “monitor”. Vegetation can act as a surrogate of both since it expresses under the conditions created by soils and hydrology, so that’s really where our main focus of the protocol lies.

## Slide 12: Lentic Monitoring: Indicators
Core Indicators
Vegetative cover and composition (LPI)
Vegetation height
Ground surface attributes
Woody species height class and age class
Use-based Indicators
Woody species use
Stubble height
Soil alteration
Covariates
Soil characteristics
Hydrology
Landscape characteristics
Land use evaluation
Contingent Indicators
Hummocks
Water Quality
Notes: Since these systems are complex we have a variety of indicators we can collect.
I’m going to discuss a few of these a little more in depth.

## Slide 13: Core Vegetation Protocol
Species inventory
Line Point Intercept (LPI) data adapted from Terrestrial AIM to better suit lentic habitats.
Vegetation heights, litter & water depths
Notes: Our core indicators are applicable across many different ecosystems and can be applied widespread because of fundamental management objectives.
Species Inventory
Line Point intercept for vegetation cover every .5 meter along transect.
Height of vegetation, depth of litter and water every 2.5 m along transect.

## Slide 14: Soil & Hydrology Covariates
Characterization of soil color and texture of soil horizons to determine indicators of hydric conditions.
Description of site hydrology, (including water source, seasonality, characteristics of surface water etc.)
Notes: Our covariate indicators aren’t meant to monitor condition and trend but rather to characterize sites for the purpose of classification, stratification, or determination of potential natural condition.
Hydrology makes wetlands! Clear indicators like surface water aren’t always present, especially in the arid west
We dig a 50 cm soil pit to characterize the color and soil horizons, looking for hydric soil indicators.Which aids in understanding longer term hydrologic conditions.
In relation to that, describe the site hydrology identify dominant water sources, seasonality which can also aid in classification.
.

## Slide 15: Annual Use Monitoring
Adapted from Multiple Indicators Monitoring (MIM) framework to measure utilization:
Woody species use
Stubble height
Soil alteration
Notes: We’ve added annual use
monitoring is conducted to evaluate utilization of these areas by ungulate species.. It’s unique that we have included annual use indicators in addition to core and contingent indicators.
This arises from a desire to link causation to condition— through collecting use data in the same location and at the same time as the condition data.

## Slide 16: Hummocks
Can lead to wetland degradation through soil compaction, erosion, and dewatering
Measure:
  Count of hummocks
  Hummock length
  Hummock depth or height
  Side angle
  Percent vegetated
Notes: Indicator that is new- not taken from already existing BLM protocol is looking at hummocks.
Hummocks or pedestal formations can be created in softer soils naturally from freeze and thaw in the winter, but often times can be exaggerated from ungulate use. We’re concerned about these formations because they can lead to wetland degredation from soil compaction, erosion, and some formation of channels that can lead to the draining of wetland. Right now we measure the angle and % vegetation cover of hummock, so we can monitor changes or improvements over time.

## Slide 17: Human Stressor Index
Evaluates stressors from surrounding landscape to the vegetation, soils, and hydrology of the monitoring plot
Notes: The last indicator I’m going to discuss is also new to BLM. The Human stressor evaluation form is a relatively rapid assessment of major land uses and stressors within and around a monitoring plot.
There is a checklist of stressors that we then define their scope of stressor ( % of an area affected by a threat) and the severity (degree of degradation at different areas).
This helps to get an idea of the degree of disturbance or potential disturbance to an area. Currently we are evaluating if this is something that might be better utilized by natural resourves specialists instead of having technicians make some of these calls in the field. This is in the pilot/protoype. There is some discussion on if having technicians make those calls is appropriate.

## Slide 18: Summer 2019: Pilot Testing
GOALS
Test protocol across variety of lentic systems
  Select target & random sites
  In-office evaluation
  Test methods and improve efficiency
  Test user variability
Notes: So now that we discussed indicators of the protocol.
This year was our pilot project. Goal- Testing the protocol on the ground for the first time and seeing how it can be implemented or holds up in a diversity of lentic systems.
We had a crew based in Colorado and one in Utah.

## Slide 19: Site Selection
300 sites randomly selected from NWI
Notes: We started by randomly selecting 300 points across BLM land in UT that were wetland areas mapped by the national wetland inventory..
From that 300 we went through a rigorous office evaluation to define sites that would be sampleable.

## Slide 20: Rejection Criteria
Office Evaluation
Access/safety issues
Size
Impounded drainage
Likelihood of wetland vegetation
Notes: Office rejection of the first 100 points was extremely high. The evaluation consisted of.
We couldn’t stick with the random design this year. Because of the amount of rejections needed we had to shift, to still work towards to goal of this project- testing the protocol on the ground. ** Because these areas in NWI are largely overmapped.
What is our criteria for moving a random point so that overall its still statistically valid. So from that we picked the most likely random sites to be sampled.

## Slide 21: Developing Rejection Criteria
Sites that look like this in the office...
...may look like this in a site visit.
Google Earth photo
PC: Richard Cope
25 m
Notes: There were times that the office evaluation looked reasonable. Google earth photos, aerial imagery, perennial vegetation..;.. Then our crew would get on the ground and it could look like this.
*Learned a lot from this. rejection criteria in the office and field is still being developed.

## Slide 22: Season Data Summary
300 sites randomly selected from NWI
29 sites visited
(12 targeted)
23 wetlands sampled
6 sites rejected
Notes: Even though we had some rejections we were still able to sample. We added 12 targeted sites. Sampled 23 wetlands with 6 rejects.
And now……

## Slide 23: Now what?
Currently….. Putting it all together!
Entering and QC’ing all data
Analyzing indicators
Reviewing methods
Revising protocol
Update electronic data capture
Notes: Putting it all together.
Figuring out how we’re analyzing indicators and ways that the data can be integrated and utilized within BLM,
Reviewing the methods, looking at efficiency and user variability.
In addition taking all of that information to help us make edits to the protocol for next season.
**We are really in the early stages of this. Huge work in progress.

## Slide 24: 2020
Utah ◉ Nevada ◉ Colorado
Idaho ◉ Wyoming
Northern California
Notes: Next Year! Questions.

## Slide 25: Thank You!
Tess Webb
trwebb@blm.gov
Justin Jimenez
jjimenez@blm.gov Joanna Lemly
Joanna.Lemly@colostate.edu
Melissa Dickard mdickard@blm.gov
BLM
CNHP
Notes: Lacking in the agency of having good botanical backgrounds and knowledge. It’s been a missing link for sometime in Utah. It’s really important for this protocol, that this is a really needed skillset which is why CNHP can work.